## Slide 1: Other nonpharmacologic biological treatments
Bipolar disorder – Maintenance treatment
Mutz J. Bipolar Disord 2023;25(1):9–24
Magnetic seizure therapy (MST): high-frequency magnetic pulses stimulate specific areas in the brain to induce a seizure
Vagus nerve stimulation (VNS): electrical stimulation of the afferent projections of the vagus nerve occurs through electrodes that are wrapped around the left vagus nerve and connected to a pulse generator implanted beneath the skin near the upper chest
Electroconvulsive therapy (ECT): an electric current is applied to the head, which induces a generalized seizure
Transcranial magnetic stimulation (TMS): a magnetic field is used to depolarize superficial neurons and initiate action potentials in the brain. TMS can target specific sites in the brain
Deep brain stimulation (DBS): electrical stimulation is delivered to specific brain regions through electrodes that are surgically implanted into the brain, and connected to a neurostimulator implanted beneath the skin just above the chest
Transcranial direct current stimulation (tDCS): a weak (0.5–2 mA) direct current is applied via scalp electrodes overlying cortical areas. As a result, the excitability of cortical tissue is altered
Notes: There is increasing interest in brain stimulation techniques, as an add-on or as an alternative to existing treatments for bipolar disorder.1 There are various such techniques, as outlined on the slide.1 However, currently the evidence regarding the use of such treatments for the prevention of relapse or recurrence in bipolar disorder is limited.1
Reference:
Mutz J. Brain stimulation treatment for bipolar disorder. Bipolar Disord 2023; 25 (1): 9–24.